## Slide 1: RECAP 24/25.02.2014
Systems & Realtime
Macros
Includes

## Slide 2: 3 Embedded Systems
Transforming System
Throughput [Bytes/s]
Data processing quality
system utilization
Reactive System
ext. Events are driving system (closed loop control systems)
Guaranteed response time
Realtime
Interactive System
short response time
High system utilization
HMI

## Slide 3: Realtime

## Slide 4: Hard Realtime (Airbag)
Incorrect if correct result does not meet with the time conditions

## Slide 5: Soft Realtime (video encoder)
Degradation, if correct result does not meet the time conditions

## Slide 6: Macros
Preprocessor instructions which replaced before the compile
Support the reusability
Platform.h or cofig.h

## Slide 7: Macros
Textual replacement
Notes: Place macros in platform.h or config.h

## Slide 8: Macros
For configuration optional if-request

## Slide 9: Includes
2 files:
  *.c: implementation, definition
  *.h: Interface/Header File: external Declaration
Local variables in *.c-File
Global varibles in *.h-File
<……> libraries
‘’……’’ h files

## Slide 10: Includes
Problem: Recursive includes
Corrective:
  Preprocessor-Definition: __<FileName>_H_

## Slide 11: Questions
Name each one example for a transfoming system, reactive system and interactive system?
TS: Video encoder, RS: PID Controller, IS: ticket selling machine

## Slide 12: Questions
Why schould placed everytime brackets on preprocessor commands with calculations?
  Example:
  #define CALC1 (2+5)
  #define CALC2 (5*3)
  In some situations it get calculated wrong.
  Int example = 10*CALC1;
  Without brackets: (10*2)+5

## Slide 13: Questions
Advantages and disadvantages of Macros
Advantages:
  Faster code
  Smalle
Disadvantages:
  Interface
  Encapsulation
  Debugging

## Slide 14: Questions
How looks the definition of the led.h-Files to avoid recursive inclusion
#ifndef__LED_H_
#define__LED_H_
//expresions of the led.h file
#endif

## Slide 15: Questions
How and where get global variables defined?
In the *.h file with the extension «extern»: extern intLED_global; Chose a good name with prefix because the Name is visible in the whole project.

## Slide 16: Questions
Is it possible to include a picture or other files than *.h-Files and libraries?
Yes, to include a bmp: #include’’bmp.txt’’