## Slide 1: INTRO FS13 Recap SW2

## Slide 2: Systems & Realtime
Transforming, Reactive, Interactive
  Trend: Heterogeneous Systems
Realtime: Correct result at the correct time
  Logical correctness
  Time in wich it is performed
Notes: Transforming
-Data processing quality
-Throughput
-Optimized system load
-Optimized Memory Usage
Reactive
-External events are driving system
-Guaranteed response time
-Control loop
-Realtime
Interactive
-Short response time
-High system load
-Human-Machine Interaction (HMI)

## Slide 3: Systems & Realtime
Hard real-time: Missing a deadline is a total system failure
Soft real-time: results after its dead-line degrades the system‘s quality of service
Notes: We can distinguish
Example Hard: Airbag
Soft: Skype

## Slide 4: Processor Expert
Components
  Methods, Properties, Events
  Generate source code
Benefits:
  Code-reuse
  Fast implementation
More Overhead
Notes: Disadvantage: Overhead

## Slide 5: Includes
„Guarding“ in the header file
  Multiple definitions/declarations
  Recursive includes

## Slide 6: C & Macros
Textual Replacement #define
  Traps
Turn off/on functionality
  #define PL_HAS_LED 1
Notes: Ben: readability, portability, configuration
Functionality : initialise or not