## Slide 1: INTRO FS13 Recap Shell

## Slide 2: Shell – For What?
Easy and universal way to configure and inspect the target, even without debugging
Notes: Easy way to configure and inspect the target without debugging

## Slide 3: Shell Connections
Notes: SRB –Board USB over USB bridge

## Slide 4: USB (Universal Serial Bus)
Device Types
  Host
    powers the bus
      PC, Laptop
  Device
    powered through the bus
      Mouse, Keyboard, ..
  OTG (On - the - go)
    Changes between 2 devices
    One device with limited host funcionality
      Camera <-> printer

## Slide 5: USB (Universal Serial Bus)
Device classes
  Communication Device Class CDC
    Modems, Network cards, …
  Human Interface Device HID
    Mouse, Keyboard, …
  Mass Storage Class MSC
    Memory –Stick, Harddisk, …

## Slide 6: USB System & Application
Asymmetrical
Up to 127 devices
Pipes for communication
  Message Pipe: bidirectional
  Stream Pipe: unidirectional
Global memory Buffer
Application polls
  Outgoing packets
  Incoming packets
  Handles control messages

## Slide 7: Shell Processor Expert component
Interfaces
  USB (CDC)
  Bluetooth (RS-232)
  Serial (RS-232)
Core of ShellPrompt
  Status
  Help
  Std I/O
Usage
  help
  status

## Slide 8: Shell interface
Notes: -shell init
-shell deinit
-shell parse

## Slide 9: Shell parser
Reads in chars and adds it to buffer
Performs USB AppTask() polling (50ms)
Parse buffer after “\r\n”
Iterates through a command table
Prints prompt and error message
Notes: Parse buffer after a certain sign

## Slide 10: Example command parser

## Slide 11
Questions ??